AldatesX User Guide
v0.9

# Introduction
AldatesX is a control system for audio/visual equipment such as video switchers and mixers. It's designed around a touchscreen interface to send commands via a controller machine to various pieces of equipment.
# The Main Screen
The main interface screen for AldatesX consists of a row of input-selection buttons along the top, a grid of output-selection buttons on the right, a toolbar along the bottom and a central area which shows device-specific controls (for example, if a camera is selected, it will show camera controls).

Image 1: Main screen, showing camera controls
Pressing an input button will display that input on the preview monitor, and will display the relevant controls in the central area of the main screen. (If there are no relevant controls for a given input, the text “No controllable device” will be displayed.) It is also possible to select inputs using the number keys 0-6 on a keyboard, if one is connected. (0 is the selection for 'Blank'.)
With an input selected, pressing one of the output buttons on the right will display that input on the chosen output. Selecting “PC Mix” will display the input behind the main visuals PC output (e.g. behind song words). This can be previewed by pressing the “PC Mix” input. Selecting “All”, or pressing the spacebar, will display the input on all outputs except PC Mix.
Note that it does not make sense to send Visuals PC to PC Mix, and it is therefore not possible to do so! It is also not possible to send a blank signal to PC Mix (this is a hardware limitation).
# Camera Control
There are three cameras in the system: two located on pillars in church, and one in the welcome area by the font. Selecting a camera input will display the camera controls, as shown in Image 1.
You can move the camera up, down, left and right by pressing the arrow buttons. It is also possible to move the cameras with the cursor keys if a keyboard is connected. You may also zoom and focus the cameras with the labelled controls. Pressing “Auto” will tell the camera to automatically focus, and it will remain in auto-focus mode until the focus+ or focus- buttons are pressed.
Backlight compensation can be toggled on or off with the Brightness+/- buttons. This is useful when the subject is against a bright background; other areas of the image might become overexposed.
Each camera has six presets available. You can store the current position, zoom and focus of a camera by pressing one of the six “Set” buttons. You can then later move the camera back to those settings by pressing the relevant number button. Presets are lost when the system is turned off. When a preset is recalled, the button is highlighted until the camera is moved.
## Advanced Camera Controls
Advanced camera controls are available by long-pressing the camera input selection buttons.

Image 2: Advanced camera controls
The advanced controls allow you to read the exact pan, tilt and zoom values from the camera, and to set the white balance mode:
- “Auto” is what the cameras default to;
- “Indoor” may be more accurate when house lights (rather than daylight) is the predominant light source in church;
- “Outdoor” is rarely going to be useful in church;
- “One Push” allows you to white-balance against a white or neutral grey card: Fill the camera frame with the card, then click “Set” when in “One Push” mode to set the white balance.
Press Back to exit the advanced controls screen.
# Extras
It is possible to connect extra inputs to the system. These can be accessed via the “Extras” screen, shown in Image 3 on page 5.
The inputs “Extras 1” through “4” are on the front of the video patch bay. The second graphics output from the visuals PC is also available on this screen.
To preview an extra input, select it and press the “Preview / PC Mix” button. Note that it is not possible to preview an extra input without also sending it to PC Mix, and vice versa.
To display an extra input on an output, select it and press the desired output, as with the usual inputs. This includes PC Mix (selecting this will also change the preview screen if a different Extras input is currently being previewed).
You can also control some functions of the “Extras” scan converter: pressing “Overscan” will toggle the overscan mode on and off, expanding the picture to fill the screen. Pressing “Freeze” will freeze the video until it is pressed a second time. (This applies only to the “Visuals PC video” input, not Extras 1-4.)
Image 3: Extras screen
# System Power
The main system power can be turned on and off through the System Power screen (Image 4 on page 6), which is displayed by pressing “System Power” in the bottom toolbar.

Image 4: System Power screen

Pressing “On” will begin a timed sequence to switch the system on. After 20-30 seconds the system should be powered up fully and the dialog box (Image 5) should disappear.
Likewise, pressing “Off” will begin a timed sequence to turn the system off. Again, after 20-30 seconds the system will be powered off and the dialog box will disappear.
You can return to the main screen at any time by pressing OK and then Back. This will not interrupt a power-up or power-down.
Image 5: System power "please wait" dialog
# Blinds and Projector Screens
The blinds and projector screens are controlled in similar ways. It is possible to raise and lower individual blinds, or all at once, and the same is true for the projector screens. You can stop the blinds or screens from moving before they reach the end of their travel.
Blinds are numbered from 1 to 6, with 1 being on the far left of church and 6 being closest to the Oak Room.

Image 6: Blinds controls

Image 7: Projector screen controls
# Advanced Functions
## System Log
The system log of the controller is viewable by pressing the Log button in the bottom toolbar. This gives technical details from the controller computer. Only the last 100 log entries are kept. This feature is intended for troubleshooting purposes. Stack traces are removed from this log; they are kept in the controller-side log files.

Image 8: System log screen
## Recalibrate Extras Scan Converter
When a computer is connected to the Extras scan converter and uses different display settings to the church computer, it may be necessary to recalibrate the image so it correctly fits the screen. This button should only be used when a full-screen, bright image such as a solid white rectangle or test card is being displayed.
## Exit AldatesX
This option exits the program. It can be restarted by tapping the icon on the desktop once.